## Slide 1
Product Description
Key Benefits
Multi-Band
NSA/SA
M2
VoLTE
Compact Size
GNSS
TCP/IP
USB 3.1
SSL
V: 2023.3
SIMCom 5G Sub-6G Module
SIM8262E-M2
SIM8262E-M2 is a Multi-Band 5G NR/LTE-FDD/LTE-TDD/HSPA+ module which supports R16 5G NSA/SA.
With a rich protocols, it is integrated with interfaces such as PCIe, USB3.1, GPIO etc. This module provides applications with great flexibility and ability of integration.
SIM8262E-M2 adopts M2 form factor. AT commands of SIM8262E-M2 are compatible with SIM8200 series modules. This also minimizes costs for customer and shortens time to market.
It is designed for applications that need huge data transmission in various wireless situations. Due to its high efficiency, security and flexibility, this module suits various applications.
M2 form factor with various interfaces
Huge data transmission
AT commands of SIM8262E-M2 compatible with SIM8200 series modules

## Slide 2
●: support o: optional * :means under developing/on-going/planning
Product |  | SIM8262E-M2
Form Factor |  | M.2
Dimensions(mm) |  | 42.0*30.0*2.3
Frequency Bands | 5G SA | n1/n3/n5/n7/n8/n18/n20/n26/n28/n38/n40/n41/n48/n66/n77/n78/n79
 | 5G NSA | n1/n3/n5/n7/n8/n20/n28/n38/n40/n41/n48/n66/n77/n78/n79
 | LTE-FDD | B1/B3/B4/B5/B7/B8/B18/B19/B20/B26/B28/B32/B66
 | LTE-TDD | B38/B39/B40/B41/B42/B43/B48
 | WCDMA | B1/B5/B8
GNSS |  | GPS/GLONASS/Beidou/Galileo/QZSS
Temperature |  | -30℃ ~ +70℃
Electrical Features |  | 
Supply Voltage(V) |  | 3.135 ~ 4.4
Data Transfer |  | 
Sub-6G SA |  | 2.4Gbps(DL)/1Gbps(UL)
Sub-6G NSA |  | 3.4Gbps(DL)/600Mbps(UL)
LTE |  | 1.6Gbps(DL)/200Mbps(UL)
HSPA+ |  | 42Mbps (DL)/5.76Mbps(UL)
Software Features |  | 
Protocol |  | TCP/IP/IPV4/IPV6/Multi-PDP/FTP/FTPS/HTTP/HTTPS/MQTTS/DNS/SSL3.0
TLS |  | ●
File System |  | ●
FOTA |  | ●
Android RIL |  | Android 6/7/8/9
USB Driver |  | Microsoft Windows Win7/Win8/Win10/Linux/Android
MBIM |  | Win8/Win10
NDIS |  | Linux/Win7/Win8/Win10
Firmware Upgrade |  | USB
Interfaces |  | 
SIM Card |  | 1.8V/2.95V
USB |  | ●
PCM |  | ●
I2C |  | ●
Diversity Receiver |  | ●
Certifications |  | 
Regulatory |  | CE(RED)*/GCF*/RoHS/REACH/TELEC/JATE